## Slide 1: Branch Prediction for the OR1200 Pipeline
Alec Roelke

## Slide 2: Outline
OR1200 pipeline overview
Motivation for branch prediction
How to handle branches in pipelines
  Stall
  Add delay slots
  Predict outcomes
Implementation of branch prediction
  Potiential improvement
Synopsys synthesis results
  Design Compiler
  IC Compiler
Conclusions and future work

## Slide 3: OR2100 Pipeline Overview
Five stages
In-order
Single-issue
ALU for Boolean logic, comparison, bit manipulation
MAC for integer arithmetic
  Multiply/divide
  Add/subtract
Optional support for floating point arithmetic
Image from www.opencores.org

## Slide 4: Motivation for Branch Prediction
Some programs have branch statements
  Function call, if, for, while, etc.
Sometimes branches are conditional
Typically, ALU is needed for calculating condition
No problem in a single-cycle machine
What to do for a pipelined machine?
i = 0
i < N
i++
TRUE
Loop Code
Post-Loop Code
FALSE

## Slide 5: Stalling
Wait until EX for branch resolution
Simplest solution
Increases CPI
IF
ID
EX
MEM
WB
BNE
…
…
…
…
1
NOP
BNE
…
…
…
2
NOP
NOP
BNE
…
…
3
T
NOP
NOP
BNE
…
4
…
T
NOP
NOP
BNE
5

## Slide 6: Delay Slot
Instruction(s) after conditional branch
Always executed regardless of branch outcome
Smallest CPI
Confusing to program for
OR1200 has one delay slot
IF
ID
EX
MEM
WB
BNE
…
…
…
…
1
DSLOT
BNE
…
…
…
2
DSLOT
DSLOT
BNE
…
…
3
T
DSLOT
DSLOT
BNE
…
4
…
T
DSLOT
DSLOT
BNE
5

## Slide 7: Branch Prediction
When a branch is fetched, predict its outcome
If prediction is wrong, flush instructions
Worst-case CPI = stall
Best-case CPI = delay slots
Many prediction schemes
A good predictor will have close to minimal CPI
IF
ID
EX
MEM
WB
BNE
…
…
…
…
1
1
BNE
…
…
…
2
2
1
BNE
…
…
3
T
NOP
NOP
BNE
…
4
…
T
NOP
NOP
BNE
5

## Slide 8: Static vs. Dynamic
Static Branch Prediction
Always predict the same value
OR1200 always predicts not-taken
  With one delay slot
  When branch is taken, one instruction is flushed
Dynamic Branch Prediction
Remember past predictions
Base current prediction on history
Not Taken
Not Taken
Taken
Taken
Branch was Taken
Branch wasn’t Taken
Branch Prediction

## Slide 9: Branch Prediction Implementation
Static branch predictor
Because of delay slot, not used until branch is already in decode
Compare target address to instruction address
  If smaller (backward branch), take branch
  If larger (forward branch), don’t take branch
Minimal changes to existing modules required
Delay slot is preserved if prediction is incorrect to maintain backwards compatibility

## Slide 10: Theoretical Performance
With no branch prediction:
Add one delay slot:
Split into and
Loops usually jump backward
  If loops are large, disappears, improving CPI by
Assumes results of conditional statements are unpredictable

## Slide 11: Design Compiler
Metric | 
Total Cell Area () | 49116.7
Clock Frequency (GHz) | 0.1
Timing Slack (ns) | -0.58
Metric | 
 | 49116.7
Clock Frequency (GHz) | 0.1
Timing Slack (ns) | -0.58

## Slide 12: IC Compiler
Used two two-port 32x32 SRAM CEL and FRAM views found in SAED 32nm PDK for register file
  Normal power consumption (rather than low power)
  Placed in center
  SRAMs mirror each other to allow for simultaneous reads of two operands and writes of one
Used dimensions 190 290
Routed up to layer 7
Since route_opt didn’t work for global routing, used route_zrt_auto instead
  As was done in the chiptop example
  Followed up with route_opt for detail routing with signal integrity options enabled

## Slide 13: IC Compiler Layout

## Slide 14: Conclusions and Future Work
Motivated the addition of branch prediction to OR1200
Implemented new static branch prediction scheme
Compiled design in Synopsys Design Compiler
Created layout in Synopsys IC Compiler
Finish implementing dynamic branch predictor
  Size will increase greatly due to required memory elements
Work out final errors in layout